Ultrasonic Presence Detector – Presence Control PRO US 360 KNX

- For indoors, particularly for rooms with obstructions in the direct sensing field of the sensor, such as partition walls, tables or angled architecture

- Dynamic all around presence detection

- Reliably detection behind objects too

- 36 m² presence detection area to detect smallest movements

- Covers the detection objects but does not penetrates through it

- Integration in the KNX System

- Optional: user remote control RC5, service remote control RC8, Smart Remote, guard cage

Technical specifications:

Voltage: 				KNX BUS voltage

Power consumption: 		30 mA

Sensor technology: 	40 KHz Ultrasonic

BUS spezifications:	4 light channels, dimmable, HLK output, presence output, twilight switch, brightness value, unlimited quantity of slaves, values changeable over the BUS, scenes, input twilight sensor for main light and basic brightness

Detection range:			ø10 m radial, ø6 m tangential/presence

Angle of coverage:			360°

Mounting height:			2.5 – 3.5 m

Light-level setting:			10 – 1000 lx

Time setting:				1-255 Min.

Mounting:				Ceiling mounting

Material:				UV-resistant plastic

IP rating:				IP20

Marks of conformity:		KEMA KEUR

Operating temperature:		-25°C to +55°C

Dimensions (H x W x D):		120 x 120 x 68 mm

Colour:				white

Warranty:				5 Years

Article number:			029463

Quantity:				___ units

Unit price:				€_____

Total price:				€_____

Contact: objekte@steinel.de