Ultrasonic Presence Detector – Presence Control PRO Single US KNX

- For indoors, in particular for hallways and long corridors

- Optimal detection in corridors or small rooms

- Dynamic all-round detection in the entire room regardless of objects and obstructions

- Covers the detection objects but does not penetrates through it

- Integration  in the KNX System

- Optional: user remote control RC5, service remote control RC8, Smart Remote, guard cage

Technical specifications:

Voltage: 				KNX BUS voltage

Power consumption: 		30 mA

Sensor technology: 	40 KHz Ultrasonic

BUS spezifications:	4 light channels, dimmable, HLK output, presence output, twilight switch, brightness value, unlimited quantity of slaves, values changeable over the BUS, scenes, input twilight sensor for main light and basic brightness

Reach:				10 x 3 m

Angle of coverage:			360°

Mounting height:			2.5 – 3.5 m

Light-level setting:			10 – 1000 lx

Time setting:				1-255 Min.

Mounting:				Ceiling mounting

Material:				UV-resistant plastic

IP rating:				IP20

Marks of conformity:		KEMA KEUR

Operating temperature:		-25°C to +55°C

Dimensions (H x W x D):		120 x 120 x 68 mm

Colour:				white

Warranty:				5 Years

Article number:			029487

Quantity:				___ units

Unit price:				€_____

Total price:				€_____

Contact: objekte@steinel.de