Ultrasonic Presence Detector – Presence Control PRO Single US COM 2

- For indoors, in particular for hallways and long corridors

- Dynamic all-round detection in the entire room regardless of objects and obstructions

- IQ mode for the automatic alignment of the stay-'ON'time to the room usage

- Optional: user remote control RC5, service remote control RC8, surface-mounting adapter AP Box, guard cage

Technical specifications:

Supply voltage:			220 – 240 V

Frequency:				50/60 Hz

Switching capacity 1:		max. 2000 W resistive load

Capacitive load / electronic ballasts: Inrush current max. 800 A / 200 μs

Switching capacity 2:		max. 230W/230V, max. 1A (cos φ = 1)
Reach:				3 x 10 m

Angle of coverage:			180°

Mounting height:			2.5 – 3.5 m

Light-level setting:			10 – 1000 lx

Stay-'ON'time:			30 sec. – 30 min.

Stay-'ON'time (switching output 2): 0 sec. – 10 min., switch-ON delay

1 min. – 2 h, stay-'ON'time

Mounting:				Ceiling mounting

Material:				UV-resistant plastic

IP rating / protection class:		IP20 / protection class II

Marks of conformity:		CE, GS

Operating temperature:		-25°C to +55°C

Dimensions (H x W x D):		120 x 120 x 73 mm

Colour:				white

Warranty:				5 Years

Article number:			007973

Quantity:				___ units

Unit price:				€_____

Total price:				€_____

Contact: objekte@steinel.de