Infrared Presence Detector – Presence Control PRO IR Quattro SLIM DALI

- For offices, conference rooms, classrooms and side rooms

- Presence detector with quadratic detection zone

- Installation almost flush to the ceiling with an installed height of just 4 mm

- Ideal for ceilings up to 4 m high

- IQ mode for the automatic alignment of the stay-'ON'time to the room usage

- Master/master and master/slave interconnections possible

- Optional: User remote control RC5, service remote control RC8, extension cable 6 m

Technical specifications:

Supply voltage:			120 – 250 V

Frequency:				50/60 Hz

Switching capacity:			max. 2000 W resistive load at 230 V

max. 1000 W resistive load at 120 V

Capacitive load / electronic ballasts: Inrush current max. 800 A / 200 μs
Reach:				Presence/radial/tangential: max. 4 x 4 m (16 m2)

Mechanically adjustable

Mounting height:			2.5 m – 4 m

Light-level setting:			100 – 1000 lx, ∞/daylight

Stay-'ON'time:			60 sec. to 15 min., pulse mode (approx. 2 sec.)

Mounting:				Ceiling mounting

Material:				UV-resistant plastic

IP rating / protection class:		IP20 / protection class II

Marks of conformity:		CE, GS

Operating temperature:		0°C to +40°C

Dimensions (H x W x D):		77 x 77 x 60 mm

Colour:				white

Warranty:				5 Years

Article number:			005795

Quantity:				___ units

Unit price:				€_____

Total price:				€_____

Contact: objekte@steinel.de