High-Frequency Presence Detector – Presence Control PRO HF 360 COM 2

- For indoors, in particular for open areas such as toilet cubicles

- HF sensor with 360° detection zone

- Detects presence through glass, wood and stud walls

- Optional concealed installation with ceiling adapter

- IQ mode for the automatic alignment of the stay-'ON'time to the room usage

- Master/master and master/slave interconnections possible

- Optional: user remote control RC5, service remote control RC8, surface-mounting adapter AP Box, guard cage, ceiling adapter for suspended ceilings

Technical specifications:

Supply voltage:			230 – 240 V

Frequency:				50/60 Hz

HF-sensor transmitter power:	approx. 1 mW at 5.8 GHz

Switching capacity 1:		max. 2000 W resistive load at 230 V

Capacitive load / electronic ballasts: Inrush current max. 800 A / 200 μs

Switching capacity 2:		max. 230W/ 230V, max. 1A (cos φ = 1)
Reach:				max. 12 m dia.

Continuously adjustable

Mounting height:			2.5 – 3.5 m

Light-level setting:			10 – 1000 lx, ∞/daylight

Stay-'ON'time:			30 sec. to 30 min., pulse mode (approx. 2 sec.)

Stay-'ON'time (switching output 2): 0 sec. – 10 min., switch-ON delay

1 min. – 2 h, stay-'ON'time

Mounting:				Ceiling mounting

Material:				UV-resistant plastic

IP rating / protection class:		IP20 with UP and IP54 with AP / protection class II

Marks of conformity:		CE, GS

Operating temperature:		-25°C to +55°C

Dimensions (H x W x D):		120 x 120 x 56 mm

Colour:				white

Warranty:				5 Years

Article number:			002848

Quantity:				___ units

Unit price:				€_____

Total price:				€_____

Contact: objekte@steinel.de