High-Frequency Presence Detector – Presence Control PRO Dual HF KNX

- For indoors, in particular for hallways and long corridors

- 2 high-frequency sensors for both directions of a corridor

- Tangential reach is limited to corridor width; no detection of movement behind closed doors

- IQ mode for the automatic alignment of the stay-'ON'time to the room usage

- Optional: Remote control RC6 KNX, remote control RC7 KNX, service remote control RC8, ceiling adapter for suspended ceilings, surface-mounting adapter Control PRO AP Box KNX, guard cage

Technical specificatons:

Power supply:			KNX bus voltage

Reach:				max. 10 x 3 m in each direction

Electronically infinitely variable

Angle of coverage:			360° with 140° angle of aperture

Mounting:				Ceiling mounting

Mounting height:			2.5 – 3.5 m

Material:				UV-resistant plastic

Settings:				Via ETS software, remote control or BUS

Light channels Light 1 – 4:	Switching/dimming, switching mode, constant lighting control, stay-ON time

Basic light level:	Permanently ON, 1 – 255 min., 1 – 100 %, all night

Stay-'ON'time:			1 – 255 Min.

Outputs:	HVAC, presence stay-ON time, light, presence, distance, movement profile, photo-cell controller, brightness level, sabotage protection

IP rating / protection class:	IP20 with UP and IP54 with AP box / protection class II

Marks of conformity:		CE, GS

Operating temperature:		-25°C to +55°C

Dimensions (H x W x D):		120 x 120 x 75 mm

Colour:				white

Warranty:				5 Years

Article number:			008802

Quantity:				___ units

Unit price:				€_____

Total price:				€_____

Contact: objekte@steinel.de