Infrared-Ultrasonic Presence Detector - Presence Control PRO

DUALTECH US KNX

- Combination of the established infrared and ultrasonic sensor technologies

- Assured detection behind objects too

- 36 m² detection area for detection of small movements

- Selection of the sensors to switch on and off

- Covers the detection objects but does not penetrates through it

- Integration in the KNX System

- Optional: user remote control RC5, service remote control RC8, Smart Remote, guard cage

Technical specifications:

Voltage: 				KNX BUS voltage

Power consumption: 		30 mA

Sensor technology: 	40 KHz Ultrasonic

BUS spezifications:	4 light channels, dimmable, HLK output, presence output, twilight switch, brightness value, unlimited quantity of slaves, values changeable over the BUS, scenes, input twilight sensor for main light and basic brightness

Reach:	US: Presence max. Ø 6m, Radial/ tangential max. 10 x 10 m (100 m2) / PIR: Presence Ø max. 3 x 3 m

Mechanically adjustable

Mounting height:			max. 3,5 m

Light-level setting:			10 – 1000 lx

Time setting:				1-255 Min.

Mounting:				Ceiling mounting

Material:				UV-resistant plastic

IP rating:				IP20

Marks of conformity:		KEMA KEUR

Operating temperature:		-25°C to +55°C

Dimensions (H x W x D):		120 x 120 x 68 mm

Colour:				white

Warranty:				5 Years

Article number:			029494

Quantity:				___ units

Unit price:				€_____

Total price:				€_____

Contact: objekte@steinel.de