Outdoor Solar SensorLight – XSolar L-S anthracite

- Outdoor solar SensorLight XSolar L-S in anthracite with infrared sensor for outdoor facades, walls and areas without electrical connection

- Low-consumption 1.2 W LED system

- No external power supply necessary, thanks to the high-performance solar panel

- Up to 60 days light availability

- Separate mounting of solar panel and bracket possible

Technical specifications:

Supply voltage:			Solar, no mains power required

Output of the lights:			1.2 W

Light colour:				4000 K

LED life expectancy:		50,000 h

Twilight setting:			2 lx

Angle of coverage:			140°

Reach:				8 m

Stay-'ON'time:			Dynamic

Basic light level:			Yes

Operating temperature:		-20 to +40°C

Material:				UV-resistant plastic

Solar panel:				monocrystalline

Mounting:				Wall mounting

Dimensions (W x H x D):		189 x 298 x 186.5 mm

IP rating / protection class:		IP44 / protection class III

Marks of conformity:		CE, GS

Warranty:				5 Years

Article number:			009823

Quantity:				___ units

Unit price:				€_____

Total price:				€_____

Contact: objekte@steinel.de