Sensor-Switched Floodlight – XLED FL-50 white

- Slave version XLED FL-50 in white for the energy-efficient lighting of large advertising panels

- Nightmatic function detects the twilight threshold and switches the light accordingly

- High colour rendering index of Ra >= 90

- Active Thermo Control protects the LEDs from overheating

- Simple interconnection with other floodlights via cable

Technical specifications:

Supply voltage:			230 V

Frequency:				50 Hz

Output:				25 W LED main lighting

Brightness:				1016 lumens

Light colour:				3500 K

LED life expectancy:		up to 50,000 h

Response brightness:		2 – 100 lx

Material:				Aluminium

Mounting:				Wall mounting

Dimensions (H x W x D):		182 x 175 x 541 mm

IP rating:				IP44

Marks of Conformity:		CE, ENEC 05

Warranty:				5 Years

Article number:			631017

Quantity:				___ units

Unit price:				€_____

Total price:				€_____

Contact: objekte@steinel.de