Infrared Motion Detector – sensIQ S white EVO

- For indoors and outdoors

- 4 highly-sensitive pyro sensors with 1360 switching zones

- 300° angle of coverage with 180° angle of aperture

- Holiday mode and permanent light configurable via remote control

- bidirectional Smart Remote communication

- Incl. remote control and corner wall mount

Technical specifications:

Supply voltage:			100 – 240 V

Frequency:		50/60 Hz

Switching capacity:	max. 2000 W (resistive load, e.g. filament bulb) at 230 V

Capacitive load / electronic ballasts: e.g. low-energy lamps, max. 800 A / 200 μs

Reach:	max. 2 - 20 m tangential, scalable in all three detection zones

Mounting height:			2.00 – 5.00 m

Detection zone:			300° with 180° angle of aperture, sneak-by guard

Response brightness:		2 – 2000 lx

Stay-'ON'time:			5 sec. to 15 min., pulse mode (approx. 2 sec.)

Permanent light:			4 h, selectable

Mounting:				Wall or corner mounting

Operating temperature:		-20°C to +50°C

IP rating / protection class:		IP54

Marks of conformity:		CE, VDE

Dimensions (H x W x D):		74 x 114 x 128 mm

Colour:				white

Included:				Remote control RC9, corner wall mount

Warranty:				5 Years

Article number:			034955

Quantity:				___ units

Unit price:				€_____

Total price:				€_____

Contact: objekte@steinel.de