Infrared Motion Detector – sensIQ S KNX stainless steel

- For indoors and outdoors

- 4 highly-sensitive pyro sensors with 1360 switching zones

- 300° angle of coverage with 180° angle of aperture

- Holiday mode and permanent light configurable via remote control

- Twilight, time and independent range setting directly on the device

- Optional: IR remote control RC1, Corner wall mount stainless steel

Technical specifications:

Power supply:			KNX bus voltage

Reach:	max. 2 - 20 m tangential, scalable in all three detection zones

Angle of coverage:			300° with 180° angle of aperture, sneak-by guard

Mounting:				Wall or corner mounting

Mounting height:			2.5 – 5.00 m

Material:				UV-resistant plastic

Settings:				Via ETS software, remote control or BUS

Light channels Light 1 – 4:	Switching/dimming, switching mode, constant lighting control, stay-ON time

Basic light level:	Permanently ON, 1 – 255 min., 1 – 100 %, all night

Stay-'ON'time:			1 sec. – 255 min.

Outputs:	HVAC, presence stay-ON time, light, presence, distance, movement profile, photo-cell controller, brightness level, sabotage protection

IP rating / protection class:		IP54 / protection class II

Marks of conformity:		CE, VDE-GS

Operating temperature:		-20°C to +50°C

Dimensions (H x W x D):		144 x 74 x 128 mm

Colour:				stainless steel

Included:				Remote control RC1

Warranty:				5 Years

Article number:			004040

Quantity:				___ units

Unit price:				€_____

Total price:				€_____

Contact: objekte@steinel.de