Light Sensor – Light Sensor Dual LiveLink

- Suitable for indoors and outdoors

- Can be configured via LiveLink app

- Light sensor with two light measurement capabilities

- Diffuse light measurement for monitoring room brightness

- Directional light measurement for monitoring areas beneath the sensor

Technical specifications:

Power supply:			24 V DALI bus voltage

Voltage consumption:		3 DALI users

Sensor technology:			Photodiode

Twilight setting:			2 -1000 lux

Mounting height:			Max. 4 m

Mounting:				Wall and ceiling mounting

IP rating:				IP54

Marks of conformity:		CE

Operating temperature:		0 to +40°C

Dimensions (H x W x D):		42 x 95 x 95 mm

Colour:				White

Warranty:				5 years

Article number:			009762

Quantity:				___ each

Unit price:				€ ____

Total price:				€ ____

Contact: objekte@steinel.de