High-Frequency SensorLight for Indoors – RS PRO LED Q1 WW silver

- For stairs, hallways and WC areas

- HF sensor with 360° detection zone

- Detects presence through glass, wood and stud walls

- Energy-efficient 26-watt LED lighting system with Active Thermo Control

- Integrated 868 MHz bidirectional wireless interconnection

- Basic light level from 10 - 50%

- Optional: Remote control RC10

Technical specifications:

Supply voltage:			220 – 240 V

Frequency:				50/60 Hz

HF-sensor transmitter power:	approx. 1 mW at 5.8 GHz

Output:				27 W LED

LED life expectancy:		50,000 operating hours

Brightness:				2350 lm

Light colour:				warm white (3000 K)

Response brightness:		2 – 2000 lx

Basic lighting level:			10  – 50%

Angle of coverage:			360°

Reach:	1 – 8 m

Stay-'ON'time:			5 sec. – 15 min.

Mounting:				Wall or ceiling mounting

Base:					Aluminium

Shroud:				PMMA

Operating temperature:		-10 to +40°C

IP rating / protection class:		IP20 / protection class II

Marks of Conformity:		CE, ENEC 10

Dimensions (H x W x D):		331 x 331 x 56 mm

Warranty:				5 Years

Article number:			007126

Quantity:				___ units

Unit price:				€_____

Total price:				€_____

Contact: objekte@steinel.de