Infrared Outdoor SensorLight – L 400S black

- Infrared outdoor SensorLight L 400S in black with crystal glass shade for outside walls and front doors

- Lamp arm made of UV-resistant plastic

- Basic light level 0% – 50%

- Reach reduction possible via shrouds

Technical specifications:

Supply voltage:			220 – 240 V

Frequency:				50/60 Hz

Output:				max. 60 W / E27

Response brightness:		2 – 2000 lx

Angle of coverage:			240° with 180° angle of aperture

Reach:				max. 12 m max. all round, temperature-stabilised

Stay-'ON'time:			10 sec. – 15 min.

Basic light level:			0% – 50%

Operating temperature:		-20 to +40°C

Material:				UV-resistant plastic

Mounting:				Wall mounting

Dimensions (H x W x D):		335.5 x 215 x 249.5 mm

IP rating / protection class:		IP44 / protection class II

Marks of Conformity:		CE, ENEC 10

Warranty:				5 Years

Article number:			611019

Quantity:				___ units

Unit price:				€_____

Total price:				€_____

Contact: objekte@steinel.de