Infrared Motion Detector – IS 3360 KNX surface-mounted, round, white

- For indoors

- 3 highly-sensitive pyro sensors with 1416 switching zones

- 360° angle of coverage with 180° angle of aperture

- For mounting heights of up to 4 m

- Reach reduction possible via shrouds

- Watches over more than 1260 sq.m.

Technical specifications:

Voltage:				KNX Bus voltage

Power consumption:		10 mA

Bus specifications:	2 light channels, dimmable, basic response brightness function for both channels,

HVAC output, presence output,   twilight switch, brightness value, unlimited number of slaves, values changable over BUS, input twilight sensor for main lighting, basic brightness, scenes

Reach:	max. 20 m tangential, reach reduction possible

Recommended installation height: 2.50 - 4.00 m

Detection zone:			360° with 180° angle of aperture

Response brightness:		2 – 1000 lx

Stay-'ON'time:			1 – 255 min.

Mounting:				Ceiling mounting

Material:				UV-resistant plastic

Operating temperature:		-20°C to +50°C

IP rating:				IP54

Marks of conformity:		CE, VDE

Dimensions (H x W x D):		ø126 x 65 mm

Colour:				white

Warranty:				5 Years

Article number:			033538

Quantity:				___ units

Unit price:				€_____

Total price:				€_____

Contakt: objekte@steinel.de