Infrared Presence Detector – Presence Control PRO

IR Quattro SLIM XS-R LiveLink

- For offices, conference rooms, classrooms and side rooms

- Super flat 360° infrared presence detector

- 16 m² square presence detection area

- Only 6 mm visible after ceiling installation

- Fits in every mounting box

- Unique retina lens

- Optional: User remote control RC5, service remote control RC8, Smart Remote

Technical specifications:

Voltage:				LiveLink DALI Bus voltage

Power consumption:		2 DALI devices

Bus specification:	Movement detection, detection range, brightness measurement, time setting, semi automatic / full automatic, teach mode, test mode, daytime mode

Sensor technology:	Passive infrared

Reach:				Presence/radial/tangential: max. 4 x 4 m (16 m2)

Segmentwise detection

restriction:				possible using blind covers

Detection angle:			360°

Response brightness:	10-1000 Lux

Time setting:				30 Sec. – 30 Min., IQ

Mounting:				Ceiling mounting

Material:				UV-resistant plastic

IP-/Protection class:		IP 20

Marks of conformity:		CE, VDE

Operating temperature:		0°C - +40°C

Dimensions (H x W x D):		Ø94 x 49 mm

Colour:				white

Warranty:				5 Years

Article number:			035235

Quantity:				___ units

Unit price:				€_____

Total price:				€_____

Contact: objekte@steinel.de