Infrared Presence Detector – Presence Control PRO

IR Quattro SLIM XS-R KNX

- For offices, conference rooms, classrooms and side rooms

- Super flat 360° infrared presence detector

- 16 m² square presence detection area

- Only 6 mm visible after ceiling installation

- Fits in every mounting box

- Unique retina lens

- Optional: User remote control RC5, service remote control RC8,    Smart Remote

Technical specifications:

Voltage:				KNX Bus voltage

Power consumption:		10 mA

Detection range:			4m x 4m  presence, tangential, radial

Bus specification

Light channels1 - 4: 	Switching/dimming, switching operation, Constant light regulation, time delay

Basic brightness: 		           Permanent on, 1-255 Min., 10-50%, whole

night,output

HLK: 					Presence dependent

Power-on delay: 			Room control, 0-255 Min.

Time delay 1-255 Min

Segmentwise detection

restriction:				possible using blind covers

Detection angle:			360°

Time setting:				1 – 255 Min.

Response brightness:		10-1000 Lux

Mounting:				Ceiling mounting

Material:				UV-resistant plastic

Settings:				Via ETS software, remote control or BUS

IP-/Protection class: 		IP 20

Marks of conformity:		CE, DEKRA, CB

Operating temperature:		0°C - +40°C

Dimensions (HxT):			Ø 94 x 49

Colour:				white

Warranty:				5 Years

Article number:			035228

Quantity:				___ units

Unit price:				€_____

Total price:				€_____

Contact: objekte@steinel.de