Infrared Presence Detector – Presence Control PRO IR Micro LiveLink

- Newly developed, high-resolution sensor system with multi-segment pyro sensor (STEINEL patent)

- ø 80 x 20,5 mm in size

- 360° angle of coverage

- 4 m x 4 m presence

- With trim for ceiling installation and mounting box

- Integration into the LiveLink system

Technical specifications:

Power supply:			DALI bus voltage

Current consumption:		2 DALI user

Sensor technology:			Passive infrared

Reach:				Presence and radial 4 x 4 m

Tangential 6 x 6 m

Recommended installation height:2.8 m

Detection zone:			360° with 90° angle of aperture

Response brightness:		2 – 1000 lux

Time setting:				1 min – 60 min, IQ mode

Mounting:				Ceiling mounting

Material:	UV-resistant plastic (casing), HDPE (lens)

Operating temperature:		0°C to +40°C

IP rating:				IP20

Marks of conformity:		CE, KEMA KEUR

Dimensions (H x W x D):		ø 80 x 20,5 mm

Colour:				White

Warranty:				5 years

Article number:			009748

Quantity:				___ each

Unit price:				€ ____

Total price:				€ ____

Contact: objekte@steinel.de