LiveLink KNX – Gateway KNX LiveLink

- LiveLink-KNX Interface for Integrating LiveLink control device in a KNX building system

- Access all LiveLink programmed light groups, light scenes, switches and sensors from KNX

- Up to 6 LiveLink systems on one LiveLink KNX interface via WLAN

- Connection over LAN interface (IP)

- Possibility of usage as programming interface for ETS (from version 3c)

Tecnical data:

Power supply:			12-30V DC, 12-24V AC

Power consumption:		<800 mA

Interface	:			Ethernet, LiveLink und KNX

Specification:

- Integration of up to 6 LiveLink Systems on one Interface

- Access to all LiveLink programmed light groups, light scenes, switches and sensors from KNX,

max. 1000 Data points

- Successful connection via LAN interface (IP)

- Can be used as programming interface for  ETS (from version 3c)

- Commisioning via ETS Software

Configuration:	KNX bus terminals, LAN connection socket RJ-45, for connection to standard WLAN-Access-Points  (10BaseT)

Assembly:	Rail mounted device for installation on DIN Rail, installation width 2 TE

Dimensions (H x W x D):		90 x 36 x 59 mm

Colour:	weiß

Warranty:	5 years

Article number:	034009

Quantity:				___ each

Unit price:				€ ____

Total price:				€ ____

Contact: objekte@steinel.de