High-Frequency SensorLight for Indoors – RS PRO 5850 LED

- For car parks, stairwells, production areas, industrial and storage rooms

- HF sensor with 360° detection zone

- Detects presence through glass, wood and stud walls

- Basic light level from 10% - 50 % dimmable

- Dust and spray-water resistant thanks to IP66

- Can be interconnected via DALI, with up to 15 slaves  per master light

- Optional: Remote control RC10

Technical specifications:

Supply voltage:			220 – 240 V

Frequency:				50/60 Hz

HF-sensor transmitter power:	approx. 1 mW at 5.8 GHz

Output:				45 W LED

LED life expectancy:		50,000 operating hours

Brightness:				5570 lm

Light colour:				cold white (4000 K)

Response brightness:		2 – 2000 lx

Angle of coverage:			360°

Reach:	Ø 2 – 8 m

Stay-'ON'time:			5 sec. – 15 min.

Mounting:				Wall or ceiling mounting

Base:					Impact-resistant plastic

Shroud:				PC, of category IK07

Basic light level:			10% - 50 % dimmable

Operating temperature:		-20 to +30°C

IP rating / protection class:		IP66 / protection class I

Marks of Conformity:		CE, ENEC 05

Dimensions (H x W x D):		1583 x 105 x 105 mm

Warranty:				5 Years

Article number:			007676

Quantity:				___ units

Unit price:				€_____

Total price:				€_____

Contact: objekte@steinel.de